## Slide 1
LinX Omnia
Easily and securely
record:
Telephones
Record analogue, ISDN (E1/T1, Q.931) and IP (SIP, SIPrec, Cisco® Built in Bridge (BiB) and H.323) telephones.
2-way Radio
Record analogue, RoIP, DMR, P25, NXDN radios and consoles (Omnitronics® RoIP, Tait® VRP and Hytera® HDAP, Zetron® RoIP).
Intercoms
Record analogue and IP (AoIP, SIP, SIPrec, RTSP) intercoms and emergency help points.
Broadcast Radio
Public Address
Air Traffic Control
Record analogue and IP (RoIP, SIP, RTSP) public broadcast radio.
Record analogue and IP (AoIP, SIP, SIPrec, RTSP)public address and announcement systems.
Records analogue and IP (ED-137, VoIP, RTSP) air traffic management (ATM) and control (ATC) systems.
Reliable stand-alone appliance for hybrid high capacity analogue, IP and ISDN audio logging and call recording with built-in hardware redundancy.
Reliable
Affordable
Secure
Hybrid
60 analogue, 60 IP & 60 ISDN recording channels
60,000 audio hours recording storage at 64Kbps
700,000 recordings DB storage
3 activation licenses for PC applications
2 years warranty
May, 2021

## Slide 2
LinX Omnia
60 analogue, 60 IP & 60 ISDN recording channels
60,000 audio hours recording storage at 64Kbps
700,000 recordings DB storage
3 activation licenses for PC applications
2 years warranty (3, 4 or 5 years optional)
Complementary firmware upgrades
Complementary remote support
Reliable Intel® & Linux ® based platform
Tamper proof file format
Export to .mp3, .wav, .spx, .afic, .au ...
Monitor, replay, reconstruct, search ...
Choice of 10 value-add PC applications
Multi-level access control
APIs: REST, Java RMI, SIP, RTSP ...
On-board network, USB and disc archiving
NTP clock, SNMP alarms, SMDR integration
Rack mount form factor: 220 x 480 x 420mm
Zinc passivated & powder coated steel
Integrated 7” colour LCD screen
Integrated keyboard
Integrated 2W speaker
Line out and headphones jack (TRS, 3.5mm)
AV-GP disks in RAID configuration
2 x gigabit network interfaces
0oC to 60oC operating temperature
100-240VAC redundant hot-swap power supply
Solid state disk (SSD) option
AMBE decoder option
2x audio storage option

## Slide 3
LinX Omnia
Analogue Recording Interface
  Capacity: up to 60 channels
  Interface: 2 wire, RJ12, 2 channels per connector
  Input impedance: >20KΩ
  Input level: -7dBm to -46dBm
  Total harmonic distortion: <2%
  Signal to noise ratio: -36dB
  CID detection: FSKR, DTMF
  Digit detection: DTMF
  Ring detection
  Automatic gain control
  Voice encoding:
    HQVQ, 8000Hz, 7.9Kbps, mono
  Frequency range: 300-3400Hz
  PIP tone: 1.4KHz, 4 levels
  Recording trigger:
    Off-Hook : 6 VDC levels (5 to 30V)
    VoX: 6 signal levels (-20dBm to -40dBm)
    Manual: on/off, via API
IP Recording Interface
  Capacity: up to 60 concurrent sessions
  Interface: Ethernet, 2 x 1GBps, RJ45
  Protocols: SIP, SDP, RTP, SIPrec, Cisco® BiB, H.323, RTSP, ED-137, Tait® VRP, Hytera® HDAP, Omnitornics® RoIP, Zetron® RoIP
  Voice encoding:
    G.711, 8000Hz, 64Kbps, mono
    AMBE, 8000Hz, 2450bps, mono
    PCM, 8000Hz, 128Kbps, mono
  Passive packet capture: via SPAN port
  Active packet capture: TCP, unicast & multicast UDP
ISDN Recording Interface
  Capacity: up to 60 concurrent calls across 4 E1/T1 links
  Interface: Hi-Z 4 wire, RJ45, E1/T1
  Protocols: ITU-T Q.931, National ISDN 1 and 2, Nortel DMS 100, AT&T 4ESS, Lucent 5ESS, Euro ISDN
  Voice encoding:
    G.711, 8000Hz, 64Kbps, mono

## Slide 4
trvr@prolancer.com.au
+61 2 8060 3311
All Australian design, development and manufacturing.
Equally popular with enterprises, governments, utilities, infrastructure, militaries ... world wide.
Total Recall VR is designed, developed and manufactured in Australia by Prolancer Pty Ltd, 2/34a Olive Street, Kingsgrove NSW 2208, Australia.
LinX Omnia